## Slide 1
An Automated Flow for Fast Generation and Verification For Custom CNN AI Accelerators on FPGA Prototyping Systems
Ahmed Emad Ibrahem
Ahmed Hossam Mohamed
Bassem Essam Abdelsadeq
Abdelrahman Khaled Mohamed
Abdelrahman Tarek Mohamed
Mohammed Ahmed Abdelqawy
Under the Supervision of Dr. Karim Ossama Abbas And Dr. Mohamed AbdelSalam
Cairo University

## Slide 2: Agenda
Motivation and Background
Methodology
Case Study and Experimental results
Future Work

## Slide 3: ML Algorithms
“strawberry”
Forward
?
“Bicycle”
“error”
Backward
Model Parameters
Forward
“Bicycle”
Deep Learning
Machine Learning
Artificial Intelligence

## Slide 4: ML Algorithms Applications
Face Recognition.
Classification.
Predict Potential Heart Failure.
Language Translation.
Autonomous Cars.

## Slide 5: Motivation
Configurations
GUI
Generate rtl
Layer Types
Input Size
Input image type ( RGB, Grayscale)
Operation Type ( fixed, float)
Number of Processing units
Perl Scripts

## Slide 6: Contributions
Previous Year:
- Layers:
    Standard Convolution Layer.
    Average Pooling Layer.
    Fully-Connected Layer.
  Features:
    Square Inputs.
    Stride 1.
  All layers are automated using Perl scripts.
  GUI interface for Perl scripts using MATLAB.
  2 Models generated to verify the layers and features.
Current Year:
  Layers:
    Depth-Wise Convolution Layer.
    Winograd-Convolution Layer.
    Max Pooling Layer.
  Features:
    Non-Square Inputs.
    Padding.
    Stride 2.
    Hard-Max Layer.
    Flatten.
    Batch-Normalization.
  All layers are automated using Perl scripts.
  GUI interface for Perl scripts using QT.
  5 Models generated to verify the new layers and features

## Slide 7: Max Pooling Layer
Implemented without using comparators.
Fixed Point: just subtract every 2 number.
Floating Point:
      1- Signs
      2- Exponent
      3- Mantissa

## Slide 8: Winograd Convolution
Winograd Operation
DP Implementation
FIFO Operation
Transform Operation
Conva & Convb Operation
Hardware Extension using Perl
Control approach with Hardware Extension
Winograd Conva & Convb Full Architecture
Pipeline Hazard Problem
Pooling Merge
Comparison With Normal Convolution

## Slide 9
+
+
+
+
+
+
+
X
X
X
X
X
X
X
X
X
+
*
1 | 0 | -1
1 | 0 | -1
1 | 0 | -1
=
10 | 10 | 10
10 | 10 | 10
10 | 10 | 10
0
Previous Operation
First : Point wise Multiplication
9 Multiplications
Second : Addition
8 Additions
1 Output Cost = 9 Multiplications + 8 Additions
4 Outputs Cost = 36 Multiplications + 32 Additions

## Slide 10
Data Window
Filter Window
First : Filter & Data Transform
Cost : 16 additions
Second: Point Wise Multiplication
Cost: 16 Multiplications
Third : Inverse Transform
Cost :8 Additions
Result
WinoGrad Operation

## Slide 11
Winograd operation Cost | Normal Operation Cost
16 Multiplications + 24 Additions | 36 Multiplications + 32 Additions
Results
Limitations
  It only efficient with 3*3 Convolution once the filter size is bigger the transformation matrix values will have numbers and it will need Multipliers
  Also it is only valid with stride 1 Convolution because It depends on the overlap of the data
  75% of models use stride 1 3*3 Convolution

## Slide 12: DP Unit Flow
FIFO
Data Transform
()
Point Wise Multiplication
Inv Transform 1
Inv Transform 2
Filter
Transform
FIFO
Filter Memory
MEM

## Slide 13: Data Insertion & FIFO Operation
FIFO
Data Window To be Processed
Wait 2 CLKS to complete another window

## Slide 14: Matrix Transform Operation
Matrix Transform Operation is nesting 2 transform matrices and we have stall Cycle so we may utilize same hardware by rewriting the equation as follows :
First Iteration
Second Iteration
First Approach:
Second Approach :

## Slide 15: Scalable Hardware
The tool allows expansion and contraction of processing units based on available resources
Whenever the computation resources are available
PERL scripts automatically generate associated RTL
.
.
.
DP Unit1
DP Unit2
DP Unit3
DP Unit N
Perl Scripts

## Slide 16: Scalable Data Paths
Mem
+
Accumulator
IFMS
Mem1
Mem2
MUX
Mem3
Mem4
DP Unit1
DP Unit1
First Step
Second Step
Mem3
Mem4

## Slide 17: Dealing with Complicated Control
Complicated Control
Block 2
Block 3
Block 1
Block 4
CU Signal Start
CU Signal End
Hazard Control
LD
DT
ML
IT1
IT1
R
DT
LD
IT2
IT2
R
Ac
W
W
LD
DT
ML
IT1
IT1
R
DT
LD
IT2
IT2
R
Ac
W
W
LD
DT
ML
IT1
IT1
R
DT
LD
IT2
IT2
R
Ac
W
W
Solution
DT
DT
ML
IT1
IT1
Acc
R
W
IT2
IT2
W
LD
R
1 Unit
LD
DT
DT
ML
IT1
IT1
Acc
R
W
IT2
IT2
W
LD
R
LD
DT
DT
ML
IT1
IT1
Acc
R
W
IT2
IT2
W
LD
R

## Slide 18: Pooling Merge
Memory
Convolution Layer
Pooling Layer
Previous Model
Winograd Model
Memory
Memory
Memory
Convolution Layer
Pooling Layer
Memory

## Slide 19: Results of the Drown Model
Winograd Model Power | Normal Model Power
0.188 W | 3.127 W
5 Layers: [ Conv-Pool-Conv-Conv-Pool ]

## Slide 20
(1x1) x M
Filters
…
(1x 1) x M
….
…
IFMs
…
( x ) x N
OFMs
Cost of Standard Convolution = x x M x N
Depthwise Separable Convolution Cost = x x M + x M x N
Reduction in cost = x 100 = () %
Depth-wise Separable Convolution
N
…
( x ) x M
…
( x ) x M
Filters
…
( x ) x M
Depth-wise
Point-wise
M
N

## Slide 21
…
…
…
( x ) x M
( x ) x M
( x ) x M
Filters
OFMs
IFMs
Depthwise Convolution
…
…
…
M
M
M

## Slide 22
(1x1) x M
Filters
…
(1x 1) x M
….
…
( x ) x M
IFMs
…
( x ) x N
OFMs
Point wise Convolution
N
…
…
…
…
…
…
M
M
M
N

## Slide 23
1
2
3
4
5
6
7
8
9
Depth-Wise
…
N
Mem
1
Bias 1
…
N
Mem
N
PS
Point-wise
Bias N
PS
…
N
…
N
Wm1 E1
Wm2 E1
WmN E1
1
2
3
4
5
6
7
8
9
Wm1 E2
Wm2 E2
Wm2E2
Design Flow
Channel 2
Channel 1

## Slide 24: Padding in CNN
        Padding is a term relevant to CNN as it refers to the number of pixels added to an image when it is being processed by the kernel of a CNN to keep the OFMSIZE equals to IFMSIZE.
2.5 | 3.5 | 2 | 3 | 2
2.5 | 4.5 | 4 | 4 | 3
2 | 5 | 5.5 | 5 | 2
2 | 4 | 4 | 4 | 3
2 | 3 | 2 | 3 | 2
0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0.5 | 0 | 0.5 | 1 | 0
0 | 0 | 1 | 1 | 0 | 0.5 | 0
0 | 0 | 0 | 1 | 1 | 0 | 0
0 | 0.5 | 0.5 | 1 | 0 | 0.5 | 0
0 | 1 | 0 | 0 | 0.5 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0
4.5 | 4 | 4
5 | 5.5 | 5
4 | 4 | 4
Output with Padding
Output without Padding

## Slide 25: Data Flow
IFM Memory
Convolution Layer
Padding
FSM
Data In
Zero
CU
DP

## Slide 26: STRIDE 2
0 | 1 | 2 | 3 | 4
5 | 6 | 7 | 8 | 9
10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24
54 | 72
144 | 162
        Stride 2 is used to reduce OFM size
Conv 3x3

## Slide 27: Data Flow
0 | 1 | 2 | 3 | 4
5 | 6 | 7 | 8 | 9
10 | 11 | 12 | 13 | 14
15 | 16 | 17 | 18 | 19
20 | 21 | 22 | 23 | 24
1
0
1
0
1
0
1
0
1
0
1
0
1
0
3
2
3
2
3
2
3
2
3
2
5
4
3
2
3
2
5
4
5
4
5
4
5
4
7
6
5
4
5
4
9
8
11
10
7
6
13
12
7
6
7
6
7
6
7
6
7
6
9
8
9
8
9
8
9
8
9
8
9
8
11
10
11
10
11
10
11
12
11
12
11
10
15
14
17
16
19
18
23
22
21
20
0
24
13
12
13
12
13
12
13
12
13
12
13
12
15
14
15
14
15
14
15
14
15
14
17
16
17
16
17
16
17
16
19
18
19
18
19
18
21
20
21
20
23
22
i_shReg_0
i_shReg_1
o_shReg_8
o_shReg_7
o_shReg_6
o_shReg_4
o_shReg_3
o_shReg_2
o_shReg_1
o_shReg_0
o_shReg_5
Dual Port Memory
Cycles needed for 1st Window =
Cycles needed for vertical shift =
Cycles needed for horizontal shift = 1

## Slide 28
DEMO

## Slide 29: Veloce Emulator
Capacity
Testability
Speed

## Slide 30: Fashion model
28 x 28 x 32
3 x 3 x 128
14 x 14 x 32
2 x 2
s = 2
Maxpool
CONV
12 x 12 x 64
Maxpool
CONV
3 x 3
s = 1
2 x 2
s = 2
3 x 3
s = 1
….
6 x 6 x 64
CONV
3 x 3
s = 1
28 x 28 x 1
FC
128
Avgpool
2 x 2
s = 2
….
10
Softmax
FC
6 x 6 x 128
Padding
Stride 2
Maxpooling
Arg-Max
Flatten

## Slide 31: Results
Maximum Clock Frequency ~ 106 Mhz
Image/sec ~ 740 Image/sec (in Python) ~ 3
Accuracy ~ 98.4% (comparing with python)
Power ~ 7.345 W

## Slide 32: AI-Agent (Drone)
208 x 278 x 32
202 x 272 x 32
207 x 277 x 32
2 x 2
s = 1
Maxpool
CONV
205 x 275 x 64
CONV
Maxpool
3 x 3
s = 1
3 x 3
s = 1
2 x 2
s = 1
….
203 x 273 x 64
CONV
3 x 3
s = 1
210 x 280 x 3
FC
FC
32
3
Softmax
Batch Normalization
Dropout
Maxpooling
Arg-max
Flatten
Non-Square input

## Slide 33: Results
Maximum Clock Frequency ~ 101 Mhz
Image/sec ~ 76 Image/sec (in Python) ~ 3
Accuracy ~ 98% (comparing with python)
Power ~ 6.101 W

## Slide 34: Future Work
Adding New features
  Inception Module
  Shuffle layer
  Skip Connection feature
  Area Tool handling
RISC-V interface with Pulpino SoC.
Dynamic Quantization

## Slide 35: Thank You…
Any Questions